## Slide 1: Wireless Triboelectric Nanogenerator
B. Sc. Martin schneider

## Slide 2: Triboelectric effect
Common Type of contact electrification
Charge seperation through seperation of adhesion
Polarity and strength of charge determined by involved materials
Crystallographic symmetry critical for tribo- and piezoelectric properties
Greatly enhanced by rubbing
Wireless Triboelectric Nanogenerator
[URL-1]

## Slide 3: Triboelectric nanogenerators
Triboelectric nanogenerators (TENGs)
  Maximize potential drop
  Easy flow of power
Polylactic Acid (PLA)
  Plant-derived
  High degree of polarization
  High electrical resistance
Graphene-PLA
  Nanocomposite with conducting graphene
  Capacity storage
  Low electrical resistance
Teflon
  High electronegativity
Wireless Triboelectric Nanogenerator
[URL-2]
Notes: High polarisation due to 2 asymmetric carbon atoms with polar groups attached

## Slide 4: Structure
Printed gPLA as bottom electrode
Teflon sheet as top electrode
~1 mm air gap between electrodes
Copper spool as wireless transmitter
Wireless Triboelectric Nanogenerator
[Mallineni et al, 2018]

## Slide 5: Structure
Increased polarisation of gPLA (b) compared to PLA (a)
  Increased output voltage
  Increased charge storage
Wireless Triboelectric Nanogenerator
[Mallineni et al, 2018]

## Slide 6: Results
Electrical Potential up to 2,4 kV
Up to 70 mW peak power
Scalably printed, mechanically robust
Wireless Triboelectric Nanogenerator
[Mallineni et al, 2018]

## Slide 7: Results
Wireless Triboelectric Nanogenerator
[Mallineni et al, 2018]
Notes: rectified

## Slide 8: Results
Wireless signal transmission
Received via band-pass filter and amplified
Wireless Triboelectric Nanogenerator
[Mallineni et al, 2018]

## Slide 9: Applications
Selfpowered wireless controllers
  Security Systems
  Home automation, smart hardware
Wireless Triboelectric Nanogenerator
[Mallineni et al, 2018]

## Slide 10: Applications
Wireless chargers
  Wasted mechanical energy → electrical energy
  ~0.2 µW/min
  Could be increased by further treatment of the electrodes
  Large arrays for walkways/roads
Wireless Triboelectric Nanogenerator
[Mallineni et al, 2018]
Notes: Full-wave rectifier

## Slide 11: References
Mallineni, S., Dong Y. et al: A Wireless Triboelectric Nanogenerator, Advanced energy materials, Vol. 8, Iss. 10, 2017
[URL-1] https://en.wikipedia.org/wiki/Triboelectric_effect (20.06.2018)
[URL-2] https://de.wikipedia.org/wiki/Polylactide (20.06.2018)

## Slide 12: Thank you for your attention!