## Slide 1: Seminar Nanobiotechnologie
B. Sc. Martin Schneider

## Slide 2: Waterproof and Tailorable Elastic Rechargeable Yarn Zinc Ion Batteries

## Slide 3: Galvanic Cells
Taylorable Yarn zinc batteries
[URL-3]
[URL-4]

## Slide 4: Production process
Carbon nanotubes
  Current collector
  Robust
  Flexible
Zn - MnO2 electrodes
  Low cost
  High specific capacity
  Eco-friendly
  ~100 µm diameter
Hydrogel-matrix
  Crosslinked polyacrylamide
  Dissolved ZnSO4 and MnSO4
  High ionic conductivity
Covered by silicone sheath
Taylorable Yarn zinc batteries
Li et al., 2018

## Slide 5: Results
1,1 m strand powered:
  100 LEDs
  100 cm2 panel
Stable while bending, knotting and stretching
Up to 300 % Strain
High cyling Stability
  98.5 % retention after 500 cycles
High waterproof capability
  96,5 % retention after 12 h underwater
Taylorable Yarn zinc batteries
Li et al., 2018

## Slide 6: Potential Uses
Textile-integrated circuits
  Wearable Gadgets
  Sportswear
  (military) uniforms
Pressure Sensors
Implantable medical devices
Taylorable Yarn zinc batteries
[URL-1]
[URL-2]

## Slide 7: References
Li H., Liu Z. et al.: Waterproof and Tailorable Elastic Rechargeable Yarn Zinc Ion Batteries by a Cross-Linked Polyacrylamide Electrolyte, ACS Nano, Volume 12, Issue 4, 2018
[URL-1]: http://www.sleepow.com/product/sleepow/ (09.06.2018)
[URL-2]: http://www.instructables.com/id/Arduino-controlled-Interactive-wallpiece/ (09.06.2018)
[URL-3]: https://en.wikipedia.org/wiki/Galvanic_cell#/media/File:Galvanic_cell_labeled.svg (10.06.2018)
[URL-4]: https://en.wikipedia.org/wiki/Alkaline_battery#/media/File:Alkaline-battery-english.svg (10.06.2018

## Slide 8: Thank you for your attention!